## Slide 1: Single Spikes SNR and Spike Shape

## Slide 2: Four measures of signal to noise ratio
The mean standard deviation across all 16 time points in the snippets.
The amp/sd at the absolute maximum
The (Max amp – Min Amp)/Average sd at max and min (obtained by averaging the variances).
The mean amp^2/var for all points in the snippets (mean SNR)

## Slide 3: Cells visually organized by FT
Clear multi-unit: multi-unit files that are made of multiple single units (usually 2 or 3 clearly sortable).
Single units obtained from multi-unit above.
Large single units – the amplitude of these cells is so large that I wanted to look at them separately.
Isolated units: Single units that did not need spike sorting - these are very clear single units in our recordings, where the amplitude is clearly above threshold…
Noise units: units that I had labeled as being noise.
M code: SnipsSNRGrouped and list_files. List files was made by selecting units from :
h52Sort_FET_Done.odt. Mat files: meanSnipsNS.mat and meanSnipsAll.mat made by running getMeanSnipsNS (non sorted) and getMeanSnipsSS (spike sorted).

## Slide 4: Example of FT Classification

## Slide 5: Standard Deviation works only to for Isolated spikes…

## Slide 6: Max-Min SNR works well with a threshold of 5!
I chose this to define well isolate single units!

## Slide 7: SNR max has issues with noise, single and large…

## Slide 8: Noise has high SNR Mean

## Slide 9: Comparing Sorted vs Non Sorted
Number of non sorted units with Min Max SNR > 5 177/583 or 30.4%
Number of sorted units with Min Max SNR > 5 914/1401 or 65.2%
Notes: Use SnipsSNRSortedvsNot.

## Slide 10: Spike Shape Sorting
I only used the spikes that had a min-max SNR greater than 5.
I also labeled some spikes by hand as: wide, large or narrow. This is a bit of a dangerous game but helps understanding the clusters.
I used a k-means on the power spectrum of the spikes (which deals nicely with phase differences, etc) with 4 groups to get clearly narrow, wide and large spikes – the fourth group is labeled unclassified but I think that they are mostly narrow spikes…
The annotation is done with annSpikeShape2.m
The sort is done with spikeShapePCA4

## Slide 11: PC1 vs PC2
All Spikes
My Annotation
K-Means Clustering
Notes: Figure 2 of spikeShapePCA4.m

## Slide 12: The third PC adds a bit more separation…

## Slide 13: 30 random spikes from each group from the k-means…
It looks great and it would look even better after lining up the peaks in time!
Notes: The unclassiffied might be narrow spikes or their own group (there are more symmetric in up vs down)

## Slide 14: Average Spike widths after sorting in ms. Measured at half maximum
Unclassified 0.21 +- 0.002 sd: 0.030
Large 0.30 +- 0.008 sd: 0.105
Wide 0.27 +- 0.002 sd: 0.038
Narrow 0.18 +- 0.001 sd: 0.020
The anova is highly significant:
  Source SS df MS F Prob>F
  --------------------------------------------------------
  Groups 2.04526 3 0.68175 239.37 1.78913e-114
  Error 2.5918 910 0.00285
  Total 4.63706 913
Notes: The number after the =- is one sem.

## Slide 15: spikeShapeResult
Results for Julie call data base are saved in spikeShapeResults.mat:
  allMeansSnips: the mean snip profile for all 1401 sorted units.
  snrMinMaxUnits: the snr value for all snips obtained for one of those 1401 units.
  indL5: index (length 487) of all units with SNR < 5.
  indG5: : index (length 914) of all units with SNR >= 5.
  allNames: cell array (length 1401) of the name of the unit
  allSortType: the sort type given during spike sorting to that unit (noise, multi, single). Not super reliable since different sorters used different strategies (e.g. Hedi called everything single).
  spikeType: the spike type obtained from the spikeShapeClustering. This is an array of size 914 – which is the number of units with indG5 == 1. To get the unit type for any unit in the dataset: if j is the index of the unit, the type is spikeType(find(indG5==j)) – as long as j is in the G5 group.
  spikeWidth: the average width of the spike snippets.